## Slide 1: A Routing Architecture for Satellite Networks
Tony Li
Juniper Networks
tony.li@tony.li
draft-li-arch-sat

## Slide 2: Disclaimers
This is a work in progress, please pardon the dust.
This is an engineering talk. Sorry, no pretty pictures.
I’m a routing guy; if I get satellite stuff wrong, please be gentle.
There’s many ways to solve this problem, this is only one.
No satellite operators were harmed as a part of this work.
Please feel free to interrupt, this is a discussion.

## Slide 3: Terminology
Internet
Local
Gateway
Satellite
Network
User
Station
Inter-Satellite
Links

## Slide 4: Issues to be addressed
Scale
  Tens of thousands of satellites
  Hundreds of gateways
Links will frequently change
  Uplinks and downlinks are continually changing
  ISLs are very flaky
Traffic engineering is a necessity
  ISLs are a limited resource

## Slide 5: Scale
Hierarchy is the only solution for scalability.
Link-state IGPs already have a two-level hierarchy.
Hierarchy also helps contain link change churn.

## Slide 6: Hierarchy in OSPF
Area 0 is the central backbone
All areas are tangent to area 0
Not a good fit for satellite topologies
Area 0
Area 1
Area 2
Area 3

## Slide 7: Hierarchy in IS-IS
IS-IS uses a two-level hierarchy
Areas are at level 1
Level 2 can be a connected subset of all areas
This allows areas to provide transit for one another
More flexible: no need for a ‘backbone’
Area 1
Area 2
Area 3
Level 2

## Slide 8: Issue: Area Partition
If an area partitions, routing falls apart
  Longstanding problem, no good fix
  Not problematic in terrestrial deployments
What about ISLs?
  Intra-orbit is better than inter-orbit, but still not reliable

## Slide 9: Stripes
Group adjacent orbits into a ‘stripe’
A stripe is the basis for a level 1 area
Assumption: for some number of orbits, we can form a stripe and avoid area partition

## Slide 10: Topology
Wrap the planet in stripes
4
1
2
6
5
3

## Slide 11: Area Proxy
New extension to IS-IS
Allows us to abstract an entire level 1 area as a single node at level 2
Drastic improvement to scalability
Area 1
Area 2
Area 3
Area 1
Area 2
Area 3

## Slide 12: Topology with Area Proxy
Level 2 routing now scales linearly with the number of areas
More level 2 connectivity is possible and doesn’t affect scalability
Area 1
Area 2
Area 3
Area 6
Area 5
Area 4

## Slide 13: Traffic Engineering
Links are not free
Network capacity is limited
Traffic engineering maps demand onto available capacity
A gateway manages link bandwidth in its region
For this, Segment Routing (SR-MPLS) seems appropriate

## Slide 14: Traffic Engineering Details
A gateway needs detailed topology information for stripes covering its region
  Participate in level 1 IS-IS directly
  Get IS-IS over a tunnel
  Get topology via BGP-LS
Monitor traffic to & from each user station to understand demand
Compute paths per user station to optimize capacity and avoid link congestion
Well established techniques in terrestrial networks

## Slide 15: Segment Routing (SR-MPLS)
Bandwidth management may need an explicit path on each packet
SR allows us to specify areas (Area SID), nodes (Node SID), and links (Adj SID) on the path
These turn into labels in the MPLS stack
Area A
Node B
Link C
Node D
Link E
Node F
IP Packet

## Slide 16: On-Stripe Forwarding
Case: user station is within the same stripe as the gateway
Forward to satellite U for the user station
Satellite downlinks the packet based on IP destination address
User station registration with satellite is out of scope
Add more labels as needed for TE
Satellite U
IP Packet

## Slide 17: Off-stripe Forwarding
Case: user station is in a different stripe from the gateway
Use an Area SID to specify the area
Satellite U
IP Packet
Area A

## Slide 18: On-stripe Return Forwarding
Case: user station returning a packet to its gateway
Assign a node SID to the gateway
Add TE labels as necessary
Protocol with the user station is out of scope
Gateway G
IP Packet

## Slide 19: Off-Stripe Return Forwarding
Case: user station returning a packet to its gateway in a different stripe
Add the area SID for the gateway’s area
Gateway G
IP Packet
Area B

## Slide 20: IP Addressing
Satellites are not using IP addresses for transit traffic
User stations are numbered from a prefix assigned by their gateway
Gateways inject their prefixes into the Internet
Rekhter’s Law: Addressing must align with topology.
Using MPLS for the forwarding plane finesses this issue: IP addresses are not part of the satellite topology

## Slide 21: Summary
Scalable routing for LEO satellites is not hard
This approach uses existing off-the shelf, production software
Scales to very large networks
Low overhead in the forwarding plane
Supports IPv4 & IPv6
Supports full traffic engineering functionality